Product Change Notice

# Reason For Change

To ensure correct operation of PCI bus masters; this affects DMA bus master transfers and in some configurations access of PCI devices to the SDRAM BAR.

This issue is caused because the three links LK12, LK13 and LK14 were shipped set to test mode.

# Description of Changes

LK12, LK13 and LK14 should be moved to position marked 1-2. This will ensure these links are set for correct operation and not test modes.

# Impact on Software

ABLE firmware version 1.95 or later will produce warnings if it detects incorrect settings.

# Date

Change must be applied to all boards shipped before 1st March 2004

# Text boxes

Product:EB110ATX

Date:08/03/2004

Reference:PCN001

## LK12

## LK13

## LK14

1

1

1

# Simtec Electronics

Web: http://www.simtec.co.uk/

Email: info@simtec.co.uk

Simtec Electronics,
Avondale Drive,
Tarleton,
Preston,
Lancs

PR4 6AX

United Kingdom

Tel: +44 (0)1772 812863
Fax: +44 (0)1772 816426